## Slide 1: Audio Signal Analysis
105501016游澈

## Slide 2: 流程示意圖
Matlab Workspace

## Slide 3: 一、音訊匯入與準備
[x, fs] = audioread('sunday.wav')
X = x(:, 1);
N = length(X);
t = (0:N-1)/fs;

## Slide 4: 二、.wav 在時域波形

## Slide 5: 二、.wav 在時域波形
1.限制
xlim([0 max(t)])
ylim([-1.1*max(abs(X)) 1.1*max(abs(X))])
2.圖表設置
grid on
xlabel('Time, s')
ylabel('Amplitude')
title(‘時域波形')

## Slide 6: 三、.wav頻譜圖

## Slide 7: 三、.wav頻譜圖
spectrogram(X, 1024, 768, [], fs, 'yaxis')
Signal
Sampling(Hanning Window)
Overlap
DFT points
Sampling Frequency

## Slide 8: 四、漢寧窗
Pictures are from National Instrument

## Slide 9: 四、漢寧窗
取漢寧窗
w = hann(N, 'periodic');

## Slide 10: 四、強度對頻率圖
[Xx, f] = periodogram(X, w, N, fs, 'power’);
Amplitude
frequency

## Slide 11: 四、強度對頻率圖

## Slide 12: 五、電壓Histogram
histogram(X)

## Slide 13: 六、強度Histogram
histogram(Xx)

## Slide 14: 七、自相關函數

## Slide 15: 七、自相關函數
[R, lags] = xcorr(X, 'coeff’);
tc = lags/fs;

## Slide 16: 八、其餘的一些分析
Max value
Min value
Mean value
RMS value
Dynamic range
Crest factor
Autocorrelation time

## Slide 17: 九、參考文獻
https://www.mathworks.com/help/signal/ref/spectrogram.html#d117e187856
https://www.mathworks.com/help/signal/ref/hann.html
https://en.wikipedia.org/wiki/Window_function
https://www.mathworks.com/help/signal/ref/periodogram.html
https://www.mathworks.com/help/matlab/ref/xcorr.html
https://zh.wikipedia.org/wiki/自相關函數
https://zh.wikipedia.org/wiki/峰質因數
Understanding FFTs and Windowing. Published by National Instrument.